AP PHYSICS C – Mechanics 1986

1.  Pulley Problem – "Count the number of support ropes!"

(c) Here we shift to a force diagram for just the 'man'.

(d) Back to 'equilibrium' with a constant upward velocity of 0.4 m/s.

Method 1: Use:

Here, we're interested in work done against gravity (by the person).

The force provided by the person is: 1000N

The distance traveled in 1 sec is:  0.4m

The time is 1 second, so...

Method 2: What if we try to use the simple formula:   ?

It looks easy but there are 2 interesting tricks involved...

(1) Because of the mechanical advantage of the pulley, Fup = 2T = 1000N vs Fg

So we only plug in:  T = 500N  for the force applied by the person.

(2) Even trickier is the 'v'. For the platform to rise 0.4m in 1 second, the rope passes

through the person's hands 0.8 m every 1sec!

Method 3: An easier way!  Just use F=1000 and v = .4 m/s  duh!

AP PHYSICS C – Mechanics 1986

2. Okay, here's the 'rolling without slipping' problem. (Fstatic and conservation of 'E')

(a)  Ei = Ef  (no sliding or kinetic friction to generate heat or loss of mechanical energy)

mgh = KT + KR  (note the 2 types of kinetic energy: Translational and Rotational)

Mgh =    Now cancel out the M and R2 and...

gh =    Now solve for v2:     v2 =

(i) KT = ½ M=

(ii) KR ==

(b) On the inclined plane (no slipping): Assuming constant acceleration down the plane...

(i)

< (from our Inclined Planed Theorem)

(ii) Using the center of the sphere as our 'pivot point' : I =   and

and  at =

(c) E =

(d) First of all, the hollow sphere (arms out) has a greater I (I recall it's ).

For the same torque, we have an 'alpha' less than that of the solid sphere:

but wait! Let's do the math... KR =  and from above

KR =  Hmm... same torque and same... !

Method 2:  Work = & Work =  (same torque, same) ...

AP PHYSICS C – Mechanics 1986

3. Restoring spring force: F = -kx3   (no friction, horizontal surface)

Answer in terms of spring constant, k, amplitude, A, and mass, M...

(a)  (This formula is a biggie!)

So to get to potential energy (U) from force (F), we have to integrate:

To get rid of the integration constant, C...

notice that F and therefore U both equal zero when x = 0, so C = 0.

U = ¼ kx4 and x = A when released, so...

(b) Maximum speed (and K.E.) will occur when U=0 (when x = 0).

K = ¼ kx4 = ½ mv2

(c) Displacement (or x) when U = K = ½ E = ½()

(Careful. I found myself plugging in ½ kx2 all the time!)

Now increase the amplitude. How is the period, T, affected? Recall that for a Hooke's     Law spring, T = , the period of oscillation was 'amplitude independent'.

(d)  F = ma  gives us: -kx3 =   vs a Hooke's Law spring:  –kx =

I can't solve this new differential equation! My old textbooks are at school and what do you know, my TI-89 solves some differential equations! CALC – deSolve(

Just enter... whoa, this is ugly! @2 is a constant and the mess = t + another constant!

Next enter some initial conditions

x(0) = a  and  v or x'(0) = 0 m/s. The TI-89 now solves explicitly for t!  Hmm, I believe @4 is a dummy variable, say 'x', so that leaves us with:

t =   Let's integrate with our calculator from  x = 0 to A = 5

just to see if the time changes when A = 10...

t =  = ?  (I got a negative time? I did get less time for A = 10.)

AP PHYSICS C – Mechanics 1986

3. Another try!   ½ mv2 + ¼ kx4 = ¼ kA4   (K + U = ETotal)

Solving for v:  v =

period, T =    Now for some BC Calculus!

Let

T = 		then

Since the integral is independent of A.		and

Except for the negative sign, both methods give:

T value of .49942 sec for A = 5 and

and half as much for A = 10.

Whew!

# Text boxes

(a) 2T = 1000N

(b) 2T – 1000 = 100(2)

2T = 1200

In parts (a) and (b), we use a force diagram of  'man + platform'.

T

Use Fnet = ma   since we're accelerating...

T + N – 800 = 80(2)

'import' T = 600 (or whatever you got in (b)!)

600 + N – 800 = 160

(1) We have to use:

M, R, h, g and

(2) Also given is rotational

inertia:   I =