WORK DEFINITIONS – AP Physics Notes                 p.1

“Work” in physics will be the transfer of energy (kinetic energy) by mechanical means.

It occurs when a force is applied in (or in the opposite) direction of a displacement.

Def #1/ Easy Definition:    All purpose, easy to remember but…

consider a 4kg mass pushed to along a floor.

If the pushing force, Fp = 5N and there is a

3m displacement to the right, then

. No problem, but if the friction force is given as:

then  and even though Fg = 40N = N (normal force), WN

And furthermore, what happens if the force (vector) acts at an angle with the displacement?

Def #2 / Trig Definition:

Suppose a rope with tension, T = 10N

Pulls a 4kg mass 3m along the floor.

If the rope makes a angle above

the horizontal, what is the work done

(by the tension force)?

Def #3/ Vector Definition:   (The “dot product” of two vectors!)

ex/ If , then

ex/ Suppose the displacement of an object is (3,4)m and the pushing force is (5,12)N,

then the work done by the pushing force is:

Think of this in two parts: The work done in the x-dirction is 5(3) = 15J and

the work done in the y-direction is 12(4) = 48J, so…

Time out for a trig and vector review!

The cosine of the angle between two vectors is:   where the numerator is a dot product and the denominator is a multiplication of two numbers.

Def #4/ Graph Definition:  What curve, you ask?

Well, if we have a force vs displacement graph, we can find the work done…

In the 1st drawing below, F = 5N and d = 3m.

In the 2nd drawing, F = 2x and d = 3m. (A variable force, like a spring!)

In the 3rd drawing, F1 = 4N for 3m and F2 = -4N for 3m. Work = 0J (hmm…)

If you wondered about the fine print below the first two drawings and also about the negative force applied in the 3rd drawing…

Def #5/ Calculus Definition:    where F is a variable function of x.

ex/ In the 1st drawing, F = 5N (constant) and x varies from 0 to 3m.

ex/ In the 2nd drawing F(x) = 2x and x also varied from 0 to 3m.

ex/ In the 3rd drawing,   (We’re not too sure at x = 3m!)

Calculate the work done by some random force like: .

(3 decimal places on the Calc AP.)

# Text boxes

T = 10N

Fp

Fg

N